## Slide 1: RETHINKING THE INTERFACE BETWEEN CIRCUITS, ARCHITECTURE, AND SYSTEMS
Samira Khan
SOLVING THE
DRAM SCALING CHALLENGE:

## Slide 2: MEMORY IN TODAY’S SYSTEM
DRAM
Processor
Memory
Storage
DRAM is critical for performance

## Slide 3: MAIN MEMORY CAPACITY
Gigabytes of DRAM
Increasing demand for high capacity
1. More cores
2. Data-intensive applications

## Slide 4: DEMAND 1: INCREASING NUMBER OF CORES
2012
2013
2014
SPARC M5
6 Cores
SPARC M6
12 Cores
SPARC M7
32 Cores
2015
More cores need more memory

## Slide 5: DEMAND 2: DATA-INTENSIVE APPLICATIONS
MEMORY CACHING
IN-MEMORY DATABASE
More demand for memory

## Slide 6: HOW DID WE GET MORE CAPACITY?
Technology
Scaling
DRAM Cells
DRAM Cells
DRAM scaling enabled high capacity

## Slide 7: DRAM SCALING TREND
Chart: START OF MASS PRODUCTION
| 1987.0 | 1990.0 | 1994.0 | 1996.0 | 1998.0 | 2000.0 | 2002.0 | 2005.0 | 2007.0 | 2010.0 | 2014.0
Y-Value 1 | 1 | 4 | 16 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
2X/1.5 YEARS
2X/3 YEARS
Source: Flash Memory Summit 2013, Memcon 2014
DRAM scaling is getting difficult

## Slide 8: DRAM SCALING CHALLENGE
Technology
Scaling
DRAM Cells
DRAM Cells
Manufacturing reliable cells at low cost
is getting difficult
WHY?

## Slide 9: In order to answer this we need to take a closer look to a DRAM cell
DRAM Cells
WHY IS IT DIFFICULT TO SCALE?

## Slide 10: A DRAM cell
Capacitor
Transistor
Contact
Transistor
Bitline
Capacitor
Bitline
LOGICAL VIEW
VERTICAL CROSS SECTION
WHY IS IT DIFFICULT TO SCALE?

## Slide 11
1. Capacitor reliability
2. Cell-to-cell interference
Challenges in Scaling
Technology
Scaling
DRAM Cells
DRAM Cells
WHY IS IT DIFFICULT TO SCALE?

## Slide 12: SCALING CHALLENGE 1: CAPACITOR RELIABILITY
Technology
Scaling
DRAM Cells
DRAM Cells
Capacitor is getting taller

## Slide 13: CAPACITOR RELIABILITY
BURJ KHALIFA
3X nm CAPACITOR
58 nm
1.45 μm
140 m
828 m
Source: Flash Memory Summit, Hynix 2012
Height to Width Ratio
6
Height to Width Ratio 25
Results in failures while manufacturing

## Slide 14: IMPLICATION: DRAM COST TREND
Chart: YEAR
| 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0
Y-Value 1 | 45 | 27 | 25 | 11 | 5 | 5 | 5 | 3 | 2 | 2 | 1.8
Y-Value 2 | 1.8 | 1.4 | 1.2 | 1 | 0.8 | 0.7
Source: Flash Memory Summit, Hynix 2012
-33%/YEAR
PROJECTION
-20%/YEAR
Cost is expected to go higher

## Slide 15: SCALING CHALLENGE 2: CELL-TO-CELL INTERFERENCE
Technology
Scaling
More interference results in
more failures
Less Interference
More Interference
Indirect path
Indirect path

## Slide 16: IMPLICATION: DRAM ERRORS IN THE FIELD
1.52% of DRAM modules failed
in Google Servers
1.6% of DRAM modules failed
in LANL
SIGMETRICS’09, SC’12

## Slide 17
ENABLE
HIGH CAPACITY MEMORY
WITHOUT
SACRIFICING RELIABILITY
GOAL

## Slide 18: TWO DIRECTIONS
DRAM
MAKE DRAM SCALABLE
Difficult to scale
NEW
TECHNOLOGIES
LEVERAGE NEW TECHNOLOGIES
Predicted to be
highly scalable
SIGMETRICS’14, DSN’15, ONGOING
WEED’13, ONGOING

## Slide 19
DRAM SCALING CHALLENGE
Technology
Scaling
DRAM Cells
DRAM Cells
NON-VOLATILE MEMORIES:
UNIFIED MEMORY & STORAGE
Non-Volatile
Memory
Storage
UNIFY
PAST AND FUTURE WORK
Detect
and
Mitigate
Reliable
System
DRAM Cells
SYSTEM-LEVEL TECHNIQUES
TO ENABLE DRAM SCALING

## Slide 20: TRADITIONAL APPROACH TO ENABLE DRAM SCALING
Unreliable
DRAM Cells
Reliable
DRAM Cells
Make
DRAM
Reliable
Reliable System
Manufacturing Time
System
in the Field
DRAM has strict reliability guarantee

## Slide 21: MY APPROACH
Unreliable
DRAM Cells
Reliable
DRAM Cells
Make
DRAM
Reliable
Reliable System
Manufacturing Time
System
in the Field
Manufacturing Time
System
in the Field
Shift the responsibility to systems

## Slide 22: VISION: SYSTEM-LEVEL DETECTION AND MITIGATION
Unreliable
DRAM Cells
Detect
and
Mitigate
Reliable System
Detect and mitigate errors after
the system has become operational
ONLINE PROFILING
Reduces cost, increases yield,
and enables scaling

## Slide 23
Detect
and
Mitigate
Reliable
System
DRAM Cells
SYSTEM-LEVEL TECHNIQUES
TO ENABLE DRAM SCALING
CHALLENGE:
INTERMITTENT FAILURES
EFFICACY OF SYSTEM-LEVEL TECHNIQUES WITH REAL DRAM CHIPS
HIGH-LEVEL DESIGN
NEW SYSTEM-LEVEL TECHNIQUES

## Slide 24: CHALLENGE: INTERMITTENT FAILURES
Unreliable
DRAM Cells
Detect
and
Mitigate
Reliable System
If failures were permanent, a simple
boot up test would have worked
What are the characteristics of intermittent failures?

## Slide 25: DRAM RETENTION FAILURE
Retention Time
Time
Leakage
Capacitor
Switch
Refreshed
Every 64 ms
Refresh Interval
64 ms
Retention Time

## Slide 26: INTERMITTENT RETENTION FAILURE
Some retention failures are intermittent
Two characteristics of intermittent retention failures
DRAM Cells
  Data Pattern Sensitivity
1
  Variable Retention Time
2

## Slide 27: DATA PATTERN SENSITIVITY
0
0
0
FAILURE
NO
FAILURE
1
1
INTERFERENCE
Some cells can fail depending on the
data stored in neighboring cells
JSSC’88, MDTD’02
Notes: Y. Nakagome, … Kiyoo Itoh, The Impact of Data-Line Interference Noise on DRAM Scaling, IJSSC’88
M. Redeker, B. F. Cockburn, and D. G. Elliott. An investigation into crosstalk noise in DRAM structures. MTDT, 2002 (Memory Technology, Design and Testing)
J. Liu et al. An experimental study of data retention behavior in modern DRAM devices: Implications for retention time profiling mechanisms, ISCA 2012

## Slide 28: VARIABLE RETENTION TIME
Chart: Time
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0
Retention Time | 512 | 512 | 32 | 32 | 32 | 32 | 512 | 512 | 512
Retention time changes randomly
in some cells
IEDM’87, IEDM’92
Notes: D. S. Yaney, C. Y. Lu, R. A. Kohler, M. J. Kelly, and J. T. Nelson, A meta-stable leakage phenomenon in DRAM charge storage – Variable hold time, 1987 IEDM Tech.
Y. Mori et al. The origin of variable retention time in DRAM. IEDM, 2005.
P. J. Restle, J. W. Park, and B. F. Lloyd. DRAM variable retention time. IEDM, 1992.

## Slide 29: CURRENT APROACH TO CONTAIN INTERMITTENT FAILURES
Manufacturing Time Testing
PASS
FAIL
1. Manufacturers perform exhaustive testing of DRAM chips
2. Chips failing the tests are discarded

## Slide 30: SCALING AFFECTING TESTING
Manufacturing Time Testing
PASS
FAIL
Longer Tests and More Failures
More interference in smaller technology nodes leads to lower yield and higher cost

## Slide 31: SYSTEM-LEVEL ONLINE PROFILING
PASS
FAIL
Not fully tested during
manufacture-time
Ship modules
with possible failures
1
2
Detect and mitigate
failures online
3
Increases yield, reduces cost, enables scaling

## Slide 32
Detect
and
Mitigate
Reliable
System
DRAM Cells
SYSTEM-LEVEL TECHNIQUES
TO ENABLE DRAM SCALING
CHALLENGE:
INTERMITTENT FAILURES
EFFICACY OF SYSTEM-LEVEL TECHNIQUES WITH REAL DRAM CHIPS
HIGH-LEVEL DESIGN
NEW SYSTEM-LEVEL TECHNIQUES

## Slide 33: EFFICACY OF SYSTEM-LEVEL TECHNIQUES
Can we leverage existing techniques?
  Testing
1
  Guardbanding
2
  Error Correcting Code
3
  Higher Strength ECC
4
WITHOUT REAL DATA ON
FAILURE RATE AND CHARACTERISTICS HARD TO ANALYZE
We analyze the effectiveness of these techniques
using experimental data from real DRAMs
Data set publicly available

## Slide 34: METHODOLOGY
Evaluated 96 chips from three major vendors
FPGA-based testing infrastructure

## Slide 35: 1. TESTING
Write some pattern
in the module
1
Wait until
refresh interval
2
Read
and verify
3
Repeat
Test each module with different patterns for many rounds
Zeros (0000), Ones (1111), Tens (1010), Fives (0101), Random

## Slide 36: EFFICACY OF TESTING
Only a few rounds can discover most of the failures
Even after hundreds of rounds, a small number of new cells keep failing
Conclusion: Testing alone cannot detect
all possible failures

## Slide 37: 2. GUARDBANDING
Chart: Time
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
Retention Time | 110 | 110 | 32 | 32 | 32 | 110 | 110 | 110 | 110 | 110
Column1 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 40 | 200 | 200
Refresh Interval
2X Guardband
4X Guardband
Adding a safety-margin on the refresh interval
Can avoid VRT failures
Effectiveness depends on the
difference between retention times of a cell

## Slide 38: EFFICACY OF GUARDBANDING

## Slide 39: EFFICACY OF GUARDBANDING

## Slide 40: EFFICACY OF GUARDBANDING

## Slide 41: EFFICACY OF GUARDBANDING
Most of the cells exhibit closeby retention times

## Slide 42: EFFICACY OF GUARDBANDING
There are few cells with large differences in retention times
Conclusion: Even a large guardband (5X) cannot detect 5-15% of the failing cells

## Slide 43: 3. ERROR CORRECTING CODE
Error Correcting Code (ECC)
  Additional information to detect error and correct data
ECC

## Slide 44: EFFECTIVENESS OF ECC

## Slide 45: EFFECTIVENESS OF ECC

## Slide 46: EFFECTIVENESS OF ECC

## Slide 47: EFFECTIVENESS OF ECC
SECDED code reduces error rate by 100 times
Combination of techniques
reduces error rate by 107 times
Adding a 2X guardband reduces error rate
by 1000 times
Conclusion: A combination of mitigation techniques is much more effective

## Slide 48: 4. HIGHER STRENGTH ECC (HI-ECC)
No testing, use strong ECC
But amortize cost of ECC over larger data chunk
Can potentially tolerate errors at the cost of higher strength ECC
5EC6ED
Notes: ECC needs t*ceil(log(k+ 1)) bits to correct t -bit errors in a k -bit input data
and one more bit to detect t + 1 bit errors.
8B SECDED: 7 + 1 bits
1KB SECDED: 13+1 bits

## Slide 49: EFFICACY OF HI-ECC
10 Years

## Slide 50: EFFICACY OF HI-ECC
10 Years

## Slide 51: EFFICACY OF HI-ECC
10 Years
After starting with 4EC5ED,
can reduce to 3EC4ED code
after 2 rounds of tests

## Slide 52: EFFICACY OF HI-ECC
10 Years
Can reduce to DECTED code
after 10 rounds of tests

## Slide 53: EFFICACY OF HI-ECC
10 Years
Can reduce to SECDED code, after 7000 rounds of tests
(4 hours)
Conclusion: Testing can help to reduce the ECC strength, but blocks memory for hours

## Slide 54: CONCLUSIONS SO FAR
Key Observations:
Testing alone cannot detect all possible failures
Combination of ECC and other mitigation techniques is much more effective
Testing can help to reduce the ECC strength
  Even when starting with a higher strength ECC
  But degrades performance

## Slide 55
Detect
and
Mitigate
Reliable
System
DRAM Cells
SYSTEM-LEVEL TECHNIQUES
TO ENABLE DRAM SCALING
CHALLENGE:
INTERMITTENT FAILURES
EFFICACY OF SYSTEM-LEVEL TECHNIQUES WITH REAL DRAM CHIPS
HIGH-LEVEL DESIGN
NEW SYSTEM-LEVEL TECHNIQUES

## Slide 56: TOWARDS AN ONLINE PROFILING SYSTEM
Initially Protect DRAM
with Strong ECC
1
Periodically Test
Parts of DRAM
2
ECC
Test
Test
Test
Mitigate errors and
reduce ECC
3
Run tests periodically after a short interval
at smaller regions of memory

## Slide 57
Detect
and
Mitigate
Reliable
System
DRAM Cells
SYSTEM-LEVEL TECHNIQUES
TO ENABLE DRAM SCALING
CHALLENGE:
INTERMITTENT FAILURES
EFFICACY OF SYSTEM-LEVEL TECHNIQUES WITH REAL DRAM CHIPS
HIGH-LEVEL DESIGN
NEW SYSTEM-LEVEL TECHNIQUES

## Slide 58: WHY SO MANY ROUNDS OF TESTS?
DATA-DEPENDENT FAILURE
Fails when specific pattern in the neighboring cell
LINEAR
ADDRESS
X-1
X
X+1
L
D
R
Even many rounds of random patterns
cannot detect all failures
0
1
0
SCRAMBLED
ADDRESS
X-4
X
X+2
0
1
0
0
1
0
X-1
X+1

## Slide 59: DETERMINE THE LOCATION OF PHYSICALLY ADJACENT CELLS
NAÏVE SOLUTION
For a given failure X,
test every combination of two bit addresses in the row
Our goal is to reduce the test time
O(n2)
8192*8192 tests, 49 days for a row with 8K cells
SCRAMBLED
ADDRESS
X-?
X
X+?
L
D
R

## Slide 60: STRONGLY VS. WEAKLY DEPENDENT CELLS
STRONGLY DEPENDENT
Fails even if only one neighbor data changes
WEAKLY DEPENDENT
Fails if both neighbor data change
Can detect neighbor location in strongly dependent cells by testing every bit address
0, 1, … , X, X+1, X+2, … n

## Slide 61: PHYSICAL NEIGHBOR LOCATION TEST
L
A
L
C
R
B
R
Testing every bit address will
detect only one neighbor
Run parallel tests in different rows
Aggregate the locations from different rows
X-4
X+2

## Slide 62: PHYSICAL NEIGHBOR LOCATION TEST
LINEAR
TESTING
0 1 2 3 4 5 6 7
RECURSIVE
TESTING
0, 1, 2, 3
0
1
4, 5
2
3
4
5
2, 3
0, 1
6
7
SCRAMBLED
ADDRESS
X-4
L
A
4, 5, 6, 7
6, 7
X
2
6

## Slide 63: PHYSICAL NEIGHBOR-AWARE TEST
27%
11%
14%
A
B
C
EXTRA FAILURES
NUM TEST
REDUCED
745654X
1016800X
745654X
Detects more failures
with small number of tests
leveraging neighboring information

## Slide 64: NEW SYSTEM-LEVEL TECHNIQUES
REDUCE FAILURE MITIGATION OVERHEAD
Mitigation for worst vs. common case
Reduces mitigation cost around 3X-10X
Variable refresh
Leverages adaptive refresh to mitigate failures
ONGOING
DSN’15

## Slide 65: SUMMARY
Unreliable
DRAM Cells
Detect
and
Mitigate
Reliable System
Proposed online profiling to enable scaling
Analyzed efficacy of system-level detection and mitigation techniques
Found that combination of techniques is much more effective, but blocks memory
Proposed new system-level techniques to reduce detection and mitigation overhead

## Slide 66
DRAM SCALING CHALLENGE
Technology
Scaling
DRAM Cells
DRAM Cells
NON-VOLATILE MEMORIES:
UNIFIED MEMORY & STORAGE
Non-Volatile
Memory
Storage
UNIFY
PAST AND FUTURE WORK
Detect
and
Mitigate
Reliable
System
DRAM Cells
SYSTEM-LEVEL TECHNIQUES
TO ENABLE DRAM SCALING

## Slide 67: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM

## Slide 68: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM
PCM, STT-RAM
NVM
Non-volatile memories combine characteristics of memory and storage

## Slide 69: VISION: UNIFY MEMORY AND STORAGE
CPU
PERSISTENTMEMORY
Provides an opportunity to manipulate persistent data directly
Ld/St
NVM

## Slide 70: DRAM IS STILL FASTER
CPU
PERSISTENTMEMORY
A hybrid unified
memory-storage system
CPU
MEMORY
Ld/St
NVM
DRAM

## Slide 71: CHALLENGE: DATA CONSISTENCY
CPU
PERSISTENTMEMORY
System crash can result in
permanent data corruption in NVM
CPU
MEMORY
Ld/St

## Slide 72: CURRENT SOLUTIONS
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
AtomicBegin {
Insert a new node;
} AtomicEnd;
Limits adoption of NVM
Have to rewrite code with clear partition
between volatile and non-volatile
Burden on the programmers

## Slide 73: OUR GOAL AND APPROACH
Goal:
Provide efficient transparent consistency in hybrid systems
Periodic Checkpointing of dirty data
Transparent to application and system
Hardware checkpoints and recovers data
Running
Epoch 0
Epoch 1
time
Checkpointing
Running
Checkpointing

## Slide 74: CHECKPOINTING GRANULARITY
DRAM
NVM
PAGE
DIRTY CACHE
BLOCK
High write locality pages in DRAM,
low write locality pages in NVM
EXTRA WRITES
SMALL METADATA
NO EXTRA WRITE
HUGE METADATA

## Slide 75: DUAL GRANULARITY CHECKPOINTING
DRAM
NVM
Can adapt to access patterns
GOOD FOR
STREAMING WRITES
GOOD FOR
RANDOM WRITES

## Slide 76: TRANSPARENT DATA CONSISTENCY
UNMODIFIED
LEGACY
CODE
DRAM
NVM
-3.5%
+2.7%
Provides consistency without
significant performance overhead
Cost of consistency compared to systems with zero-cost consistency

## Slide 77
DRAM SCALING CHALLENGE
Technology
Scaling
DRAM Cells
DRAM Cells
NON-VOLATILE MEMORIES:
UNIFIED MEMORY & STORAGE
Non-Volatile
Memory
Storage
UNIFY
PAST AND FUTURE WORK
Detect
and
Mitigate
Reliable
System
DRAM Cells
SYSTEM-LEVEL TECHNIQUES
TO ENABLE DRAM SCALING

## Slide 78: OTHER WORK
CPU
MEMORY
STORAGE
IMPROVING CACHE PERFORMANCE
MICRO’10, PACT’10, ISCA’12, HPCA’12, HPCA’14
EFFICIENT LOW VOLTAGE PROCESSOR OPERATION
HPCA’13, INTEL TECH JOURNAL’14
NEW DRAM ARCHITECTURE
HPCA’15, ONGOING
ENABLING DRAM SCALING
SIGMETRICS’14, DSN’15, ONGOING
UNIFYING MEMORY & STORAGE
WEED’13, ONGOING

## Slide 79: FUTURE WORK: TRENDS
CPU
MEMORY
STORAGE
DRAM
NVM
LOGIC

## Slide 80: APPROACH
DESIGN AND BUILD BETTER SYSTEMS
WITH NEW CAPABILITIES
BY REDEFINING FUNCTIONALITIES ACROSS DIFFERENT LAYERS
IN THE SYSTEM STACK

## Slide 81: RETHINKING STORAGE
APPLICATION
OPERATING SYSTEM
SSD
CPU
FLASH
CONTROLLER
FLASH
CHIPS
What is the best way to design a system
to take advantage of the SSDs?
APPLICATION, OPERATING SYSTEM, DEVICES

## Slide 82: ENHANCING SYSTEMS WITH NON-VOLATILE MEMORY
How to provide efficient instantaneous system recovery and migration?
Recover
and
migrate
NVM
PROCESSOR, FILE SYSTEM,
DEVICE, NETWORK, MEMORY

## Slide 83: DESIGNING SYSTEMS WITH MEMORY AS AN ACCELERATOR
SPECIALIZED CORES
MEMORY WITH LOGIC
MANAGE
DATA
FLOW
How to manage data movement when applications run on different accelerators?
APPLICATION, PROCESSOR, MEMORY

## Slide 84
THANK YOU
QUESTIONS?

## Slide 85: RETHINKING THE INTERFACE BETWEEN CIRCUITS, ARCHITECTURE, AND SYSTEMS
Samira Khan
SOLVING THE
DRAM SCALING CHALLENGE: